## Slide 1: ED5502 Embedded Software
Lecture 7:
STM32 Timer/Counters (1): Introduction and Setting Time Periods
Ciaran MacNamee

## Slide 2: What we will cover today
Timer/Counters – general ideas
Timers/Counters as counters with various clock inputs
Timer/Counter use – tick or similar applications

## Slide 3: After these lectures you should be able to:
Initialise and use the STM32L476RG Timer/Counters to generate Timer Periods (Ticks), Output Signals, and Measure Times, Counts and Frequencies of input signals
In this lecture, we generate a time delay or period

## Slide 4: STM32L476RG Timer/Counters
Arm Cortex-M3/M4 all have a SysTick timer
STML476RG also has two Basic Timers
  TIM6 & TIM7
One Low Power Timer
  LPTIM
7 General Purpose Timers (2 Groups)
  TIM2, TIM3, TIM4, TIM5 and TIM15, TIM16, TIM17
2 Advanced Control Timers
  TIM1 & TIM8
Many of these are common across all STM32 MCUs - Often having the same name for compatibility and reuse reasons

## Slide 5: Arm Cortex-M3/4 SysTick Timer
SysTick is available on the Cortex core
  So it’s on any Cortex-based microcontroller
  Intended for use as an Operating System tick
  Having it in the core makes portability easier
  We could use it for our setting time delays – but only if we do not have an Operating System (OS)
The SysTick counter has 24-bits
STM32L476RG SysTick

## Slide 6: Arm Cortex-M3/4 SysTick Timer
SysTick is available on the Cortex core
  So it’s on any Cortex-based microcontroller
  Intended for use as an Operating System tick
  Having it in the core makes portability easier
  We could use it for setting time delays – but only if we do not have an Operating System (OS)
The SysTick counter has 24-bits
We have been using SysTick already without knowing it
All code generated by CubeMX uses SysTick, for example HAL_IncTick() and HAL_Delay(500);

## Slide 7: Timer/Counters
Very widely used on-chip peripherals in many MCU applications
  Found in one form or another on most microcontrollers
Typical uses:
Periodic Events, Ticks or Interrupts
Measure Time Periods
Determine Pulse Widths
Measure Speed
Measure Frequency
Generate Output Signals

## Slide 8: Microcontroller Timer/Counters
Most of today’s microcontrollers have more than one Timer/Counter
We will see that the programmer’s view of the Timer/Counter is:
Control Register(s)
Status Register(s)
Data Register (The Counter/Timer Count Register)
Again, this is the general view of on-chip peripherals in any microcontroller

## Slide 9: Timer/Counters
Essentially Timer/Counters are simply up-counters or down-counters
For timing, the counters are counting time periods at their inputs (e.g. an internal or external clock)
For counting, they count events or pulses or similar
Or count events in a given time, by making these events the input to the counter, and checking the count periodically – e.g. engine driveshaft RPM
Even very simple microcontrollers have at least one timer/counter system

## Slide 10: Four Bit Up Counter
Counts to 15 (all ones) then wraps around to Zero
Cout (Carry Out) indicates the rollover
You can generalise this idea to counters of any size
The D and Load* inputs allow loading of a start value other than zero
General Idea
0000 -> 0001 -> ….1110->1111->0000->0001
Cout
Clock Input
You can extend this idea to a larger number of bits

## Slide 11: Four Bit Down Counter
Counts to 0 (all zeroes) then wraps around to all ones
Cout (Carry Out) indicates the rollover
You can generalise this idea to counters of any size
The D and Load* inputs allow loading of a start value other than zero
General Idea
1111 -> 1110 -> ….0010->0001->0000->1111
Cout
In both up and down cases Cout can be used to extend the effective number of bits
You can count Cout occurrences to extend the counter
Clock Input

## Slide 12: Extending the Counter
A 4 bit counter would be pretty useless to us
Microcontroller counters come in 8-bit, 16-bit and 32-bit variants mostly
Even the 16-bit counters can reach their maximum or minimum count quickly
Clock Input
Two solutions
Detect the Overflow or Underflow event and use it to update a software counter – you can extend the count to an arbitrary length
Divide down (Prescale) the clock input so it’s clocked by a lower frequency input – reduced precision but longer effective counting
0000 -> 0001 -> ….1110->1111->0000->0001
Cout
Count Cout
Divide by N

## Slide 13: Four Bit Up Counter for events
Connect the Clock Input to an event detector to enable event counting
Sensor Output

## Slide 14: Four Bit Up Counter timing delays
Option1:
Connect the Clock Input to a clock input of known frequency
Load the counter with a known value
Count until rollover gives your delay or tick
Works well with down counters too
Clock Signal
Option2:
Connect the Clock Input to a clock input of known frequency
Load the counter with zero, load a comparison counter with a set value
Count until the counter reaches the comparison counter – the time taken gives your delay or tick

## Slide 15: Four Bit Down Counter timing delays
Option1:
Connect the Clock Input to a clock input of known frequency
Load the counter with a known value
Count down until rollover gives your delay or tick
Clock Signal
Option2:
Connect the Clock Input to a clock input of known frequency
Load the counter with a reload counter value
Count until the counter reaches zero – the time taken gives your delay or tick, and automatically reloads the counter

## Slide 16: Four Bit Up Counter Input Capture
Connect the Clock Input to a clock input of known frequency
Capture the Counter Value when an event occurs
Save the Counter Value
Capture the Counter Value again when the next event occurs
The difference between the counts tells you the time between the occurrences of the event
Clock Signal
Capture Register
Capture Event
Save to memory before the occurrence of the next event

## Slide 17: Four Bit Up Counter Output Generation
Connect the Clock Input to a clock input of known frequency
Start at zero
Compare with a known preset value
When they match you have made your delay or tick
Clock Signal
Compare Value
Comparator
Delay Generated or Event Occurrence
The Event Occurrence can be sent to an output pin
You can generate an output signal this way
E,g. for motor control (PWM)

## Slide 18: Typical Uses of Timers/Counters
Typical uses:
Periodic Events, Ticks or Interrupts
Measure Time Periods
Determine Pulse Widths
Measure Speed
Measure Frequency
Generate Output Signals
Let’s start with a Periodic Event
We will use TIM2 General Purpose Timer

## Slide 19: Setting a Timer Tick or Delay
The idea is simple
What delay do we want?
Choose a clock source that will easily generate this time (Time per clock below)
Time = Timer Count Value * Time per clock
Set the Timer Count Value by writing this data to the Timer’s Automatic Reload Register (ARR)
Start the timer
Wait until the timer reaches the ARR value
Notes: This is very wasteful on CPU resources
We will see that this kind of application is better implemented using interrupts

## Slide 20: First Step: which bus?
Remember: we need to know this to find the RCC_ENR register with our timer’s clock enable bit
Nothing happens until this bit has been set

## Slide 21: First Step: which bus?
We see that TIM2, TIM3, TIM4, TIM5 are on the APB1 Bus
TIM1, TIM8 and others are on APB2

## Slide 22: RCC_APB1ENHR
This bit for TIM2

## Slide 23: Timer Structure (TIM1 as example)
Master-Slave Controller
Timebase
Timer Channels
Break Feature

## Slide 24: Master-Slave Unit
Provides the time-base unit with the counting clock signal and the counting direction control signal
Mainly provides the control signals for the time-base unit.
Sets the counting configuration for the time-base unit
Sets the counting status
Its Trigger Out (TRGO) signal could be Trigger In (TRGI) to another Timer

## Slide 25: Time-Base Unit
Includes the timer counter, a prescaler stage and a repetition counter
Timer counter is controlled by two registers:
TIMx_CNT: to read and write the timer counter
TIMx_ARR: timer counter reload value
Also triggers a timer ‘update event’ when a new counting cycle is restarted, depending on the value of the repetition counter
If non-zero: no event
Notes: TIMx_ARR: timer counter reload value
  Up-counting: when the timer reaches the TIMx_ARR value, the timer resets itself and a new counting cycle is restarted
  If down-counting and reaches zero value, the timer counter value is set to the content of TIMx_ARR and a new counting cycle is restarted

## Slide 26: Timer Channels Unit
In general, this is the connection of the Timer Counter to the microcontroller pins – input or output (with a few exceptions)
Break Unit
For Timers with complementary outputs, the break unit can ensure safe shutdown

## Slide 27: TIM2/TIM3/TIM4/TIM5

## Slide 28: TIM2/TIM3/TIM4/TIM5

## Slide 29: TIMx Control Register 1
Only Relevant Bits shown

## Slide 30: TIMx Control Register 1
Relevant Bits
TIMx_CR2 is not relevant for now

## Slide 31: TIMx Status Register
Relevant Bits

## Slide 32: TIMx Event Generation
Relevant Bits

## Slide 33: TIMx Counter Register
Some GP Registers are 16-bits
TIM2 is always 32-bits across all STM32 MCUs

## Slide 34: TIMx Prescale Register

## Slide 35: TIMx Auto-Reload Register

## Slide 36: Time Delay Example (STM32 App Note)

## Slide 37: What Time Delay?
The target delay will guide us to what prescaler setting we use and what count we set
Let’s say 1 second (f = 1 Hz)
Our SYSCLK runs at 80 MHz – look at the TIM2 clocking schemes next

## Slide 38: SYSCLK and TIM2 Clock
Clock source for TIM2..7 is here
PCLK1 is at 80 MHz

## Slide 39: Generating 1 Hz event (1 sec delay)
Let’s Prescale TIM2 by 8000
80MHz/8000 = 10kHz, T = 0.1ms
Count 10000 * 0.1ms = 1 second
// configure TIM2 to wrap around at 1 Hz
RCC->APB1ENR |= 1; /* enable TIM2 clock */
TIM2->PSC = 8000 - 1; /* divide by 8000 */
TIM2->ARR = 10000 - 1; /* divided by 10000 */
TIM2->CNT = 0; /* clear timer counter */
TIM2->CR1 = 1; /* enable TIM2 */
while (1) {
while(!(TIM2->SR & 1)) {} /* wait until UIF set */
TIM2->SR &= ~1; /* clear UIF */
/* Do something useful, eg toggle LED */
}

## Slide 40: Summary
Looked at Timer/Counters in general
Introduced STM32 Timers
A lot of common features across the product range
Looked at some of the General Purpose Timer Registers – those relevant to generating a clock tick