## Slide 1: ED5502 Embedded Software
Lecture 10:
STM32 Timer Modes,
Input Capture Interrupts
Ciaran MacNamee

## Slide 2: What we will cover today
We look at the Compare/Capture features of STM32 Timers
We look at how to set up a Timer for Input Capture (IC) using IC interrupts

## Slide 3: After these lectures you should be able to:
Explain the use of the Capture/Compare features of the STM32 timers
Explain how the HAL libraries describe the Timer Registers
Initialise and use Timer Interrupts starting with ST32CubeMX

## Slide 4: Input Capture using MCU Timers
Given a free running counter, an event (usually a rising or falling edge of an input signal) causes the current counter value to be captured into a register, providing a timestamp of the event
If you save the timestamp, and allow the next event to capture a subsequent counter value, then the difference between the timestamps is the number of clocks between events
If you know the clock period, you can calculate the time difference

## Slide 5: Four Bit Up Counter Input Capture
Connect the Clock Input to a clock input of known frequency
Capture the Counter Value when an event occurs
Save the Counter Value
Capture the Counter Value again when the next event occurs
The difference between the counts tells you the time between the occurrences of the event
Clock Signal
Capture Register
Capture Event
Save to memory before the occurrence of the next event

## Slide 6: Example using Input Capture
Input Signal

## Slide 7: STM32 Timers
STM32 has four types of Timer:
Advanced-Control Timers (TIM1/TIM8)
  16-bit timers with master-slave and break features
General-Purpose Timers (TIM2/TIM3/TIM4/TIM5)
  TIM2 and TIM5 are 32-bit timers
  TIM3 and TIM4 are 16-bit timers
Basic Timers (TIM6/TIM7)
  No connection to IO pins (Channels)
Low Power Timer (LPTIM)

## Slide 8: General Purpose Timers
These timers may be used for time delays or for output (compare) signal generation or for input capture
Output Compare (including PWM) changes the state of an output pin (Channel in STM32)
Input Capture detects an edge on an inout pin (or channel)
These timers support 4 channels

## Slide 10
You can clock the Timer’s Counter from an External Signal
These are the Timer Inputs (also the Outputs)

## Slide 11: Timer Components
We can think of three components
Control Block
  Selects clock sources and enables, including triggers in and out
The Timer Time base unit
  Includes the timer counter (CNT) and auto-reload register
Input and output functionality
  Compare/Capture Registers and Channel connections

## Slide 12
Trigger and Clocks

## Slide 13
Time Base Unit
Counter, ARR

## Slide 14
Capture Compare Registers
And Channels
Inputs to the left
Outputs to the Right
(Same pins used)

## Slide 16: Time Base Unit
No matter what mode we use for the Timer/Counter, we have to set up options to control the Time Base Unit
These options must be setup to enable Input Capture too
Clock and Prescaler affect timing resolution

## Slide 17: Auto-Reload Register and Update Events
You must set ARR to a value > 0
or counting will not start
You can also count down or even up and down

## Slide 18: Control Registers
Sets Direction, ARR Source, whether an Update Event updates the counter etc
CCDS enables DMA mode
We will see how these registers map to STM32CubeMX and to HAL TypeDefs

## Slide 19: Example: TIM2 CH1 Input Capture
We will configure TIM2 CH1 for Input Capture
First, what pin does this map onto?
See STM32L476RG Data Sheet, Alternate Functions

## Slide 20
We could use PA0 or PA5
Both are on the Arduino Headers
Use PA0 this time

## Slide 21: STM32CubeMX: PA0
We used this pin for ADC1_IN5 in the past
Next select TIM2 under Timers

## Slide 22: STM32CubeMX: PA0
Channel 1, Select Input Capture Direct Mode
(We’ll see why shortly)
This opens up the Configuration and Parameter Settings

## Slide 23: STM32CubeMX: PA0
The Clock Frequency is 80MHz
Divide by 0 will give a TIM2 Clock frequency of 1 MHz, Period = 1 us
Select 0xffffffff (8 f’s – max count for a 32 bit counter)
Up counter
No division of the internal clock

## Slide 24: STM32CubeMX Generated Code
This example refers to TIM1, but TIM2 is similar
Calls HAL_TIM_IC_Init(&htim1);
IC means Input Capture here

## Slide 25: HAL_TIM_IC_Init()
This is found in stm32l4xx_hal_tim.c

## Slide 26: HAL_TIM_IC_Init()
This is found in stm32l4xx_hal_tim.c

## Slide 27: HAL_TIM_IC_Init()
Here is the typedef used
*Instance is just a pointer to the Timer we’re using, eg TIM2

## Slide 28
Trigger and Clocks
Trigger and Master Slave options are also initialised
(Even if not used)

## Slide 29: Triggers, Master/Slave Options
For Input Capture, if you’re not using these options, you could probably leave them at their default conditions (unused or not enabled, but CubeMX generated code may include initialisations of these conditions
(Trigger Outputs are sent to slave timers)

## Slide 30: CubeMX and Input Capture Options
These correspond to bit settings in the Timer (Capture Compare) Control Register Settings

## Slide 31: TIMx_CCMRy Registers

## Slide 32: TIMx_CCMRy Registers
Depending on the setting of these fields, the upper or lower rows determine what’s enabled
This register applies to CH1 & CH2
CCMR2 applies to CH3 & CH4
The lower row applies to Input Capture

## Slide 33: TIMx_CCMRy Registers
This is what is being selected here
This is Direct Input Capture

## Slide 34: TIMx_CCMRy Registers
The other bits select input filter prescaler and other options

## Slide 35: CCMRx Registers: CubeMX code
This screen capture was for TIM1 CH2, but the idea is the same

## Slide 36: CubeMX TIM2 CH1 NVIC Settings
Enable TIM2 Interrupt and set priorities (if using)

## Slide 37: CubeMX TIM2 CH1 NVIC Settings
Enable TIM2 Interrupt and set priorities (if using)
Appears here because we set it in the TIM2 NVIC field

## Slide 38: CubeMX TIM2 CH1 NVIC Settings
Make sure that Interrupt handler code is generated and that initialisation code is generated

## Slide 39: Input Capture Interrupt Init and start
This example is for TIM1 CH2, but TIM2 CH1 would be similar
Note that I included this in the USER CODE BEGIN – END block
This is needed to start input capture
IT means do this with Interrupt enabled

## Slide 40: Input Capture Interrupt Handler (ISR)
TIM1 & TIM2 are slightly different
TIM1 has a dedicated capture interrupt
TIM2 has a general interrupt for all its IRQs
But its (CubeMX/HAL) handler will check for the interrupt source and call the Capture Handler – Capture Callback
We can find the __weak version in the Timer HAL, stm32l4xx_hal_tim.c
Next slide shows where to find it (and similar code)

## Slide 41
Drivers/STM32l4xx_HALDrivers/Src/stm32l4xx_hal_tim.c
Now browse through function list in the RHS pane

## Slide 42: Capture Callback Handler shell
Now we can copy this (without the __weak attribute) to our code to build our handler
Delete the body and add our own

## Slide 43: Example using Input Capture
Input Signal
We need two variables for the captured data
We can ping-pong them for following edges

## Slide 44: Example using Input Capture
Input Signal
But our timer is free running – so it could overflow between captures
Our calculation has to account for this
(This is less likely with the 32-bit counter.
In this case I also assume that the relative counter clock and input signals only cause one overflow)
Project 2: only one rollover is possible

## Slide 45: Capture Callback
Use two variable (here in an array) for capture values and a counter to keep track
Use HAL_TIM_ReadCapturedValue() to get the captured register (you could also read TIM2 CCR1 register if not using the HAL)

## Slide 46: More Capture Callback
We store successive captures
I am going to do the difference calculation here, so I use static local variables, but in your project, these may need to be global because they will be used in the main while(1) loop
I also introduce a completed flag

## Slide 47: Capture Callback – Clock Difference
To keep everything relatively simple, I did everything in the ISR. In your case, you want to calculate frequency and report to the user, so the calculations would probably be in main- while(1)

## Slide 48: Difference calculation - Notes
If captures[1] > captures[0], the count difference is obvious, but if captures[0] > captures[1], then there has been a rollover
If there was a rollover, then the counter counted to it maximum value and started again
  Count difference = time to rollover + time to captures[1], time to rollover = max count – captures[0]
Strictly max count is the ARR register, for this 32-bit case I knew I had set it to 0xffffffff

## Slide 49: Difference calculation - Notes
To get the Time Difference (and hence the frequency) you should multiply the number of clock cycles by the time per clock
In this example, I knew that the PCLK source to TIM2 was 80 MHz, and the prescaler was set to divide by 80, so each clock was 1us
  1 us is a good choice for the frequencies we’re using
Strictly, you should use a HAL library to get the ABP1 PCLK1 frequency and then scale this value with the prescaler

## Slide 50: Difference calculation - Notes
In your application, you should return the data to the while loop and do the calculations (especially reporting data to the user) after exiting the interrupt handler
This code just uses the Green LED on the Nucleo board as a status indicator (greater or less than 5kHz (200us period))

## Slide 51: Difference calculation - Notes
This code is running on TIM2
TIM1 code is similar but note that the maximum count is 0xffff not 0xffffffff because it’s a 16-bit timer
(In fact, in all cases it is set by the ARR setting – I initialised ARR to 0xffff for TIM1 and 0xffffffff for TIM2)

## Slide 52: Summary
Worked example using CubeMX and the HAL libraries to implement a measurement of a periodic signal using the STM32 bit counter in input capture mode