## Slide 1: ED5502 Embedded Software
Lecture 14:
STM32: FreeRTOS Example
Ciaran MacNamee
See www.freertos.org for FreeRTOS

## Slide 2: At the end of this lecture you should be able to:
Distinguish between hard real-time and soft real-time systems
Explain the limitations of foreground / background systems operation
Describe how a real-time kernel organises and schedules tasks
Explain the states that a task can be in
Write the outline of a task to run in a real time operating system or kernel

## Slide 3: Real Time Systems: Hard and Soft RT
Think of real-time systems as being systems where events must occur within a fixed time period
  The timing behaviour of a system is as important as its logical correctness
Real-time systems can be soft real-time or hard real-time
Soft real-time: tasks are performed as fast as possible, but don’t have to finish by specific times
Hard real-time: tasks have to be performed correctly but also on time
  Most hard real-time systems are embedded

## Slide 4: Begin with CubeMX
We use the Nucleo-64 with Defaults
Then enable some GPIO Outputs

## Slide 5: MiddleWare -> FreeRTOS
Only one possible entry in the drop down
These are the types of services you expect in the RTOS
Accept the defaults for now

## Slide 6: System Tick
We have to change the SYS Timebase source from SysTick
We change it to the Basic Timer TIM6

## Slide 7: Next Define our Project
Generate Code and open our project as usual

## Slide 8: Project in TrueStudio

## Slide 9: Project in TrueStudio
These files are new
Note include cmsis_os.h

## Slide 10: Adding Tasks in FreeRTOS
We will add two tasks to the FreeRTOS code, to toggle LEDs at different frequencies
FreeRTOS documentation gives this API to show how to create a Task
Prototypes to create two tasks
Task Code (ie Task Function)
Name For documentation only
Each task needs a stack
Passed in parameters
Priority (High numbers – higher priority)!
Task Handle (could be used to change priority)

## Slide 11: FreeRTOS Delay
This delay is different from the ones we have used
It places the task in the Blocked mode for a fixed number of , so that other tasks can run Tick Interrupts - the task does not use any processing time while it is in the Blocked state

## Slide 12: FreeRTOS LED Toggle Tasks
Slight differences in the two tasks
Then just Build and Go as usual
(First compile may be slow)

## Slide 13: FreeRTOS Task
We omitted this – if our code exits the infinite it should delete itself

## Slide 14: Summary
Getting started with FreeRTOS in STM32 with CubeMX is fairly straightforward