## Slide 1: ED5502 Embedded Software
Lecture 4:
STM32L476RG & Nucleo64
Bitwise operators in C
STM32 Parallel Ports
Ciaran MacNamee

## Slide 2: What we will cover today
STM32L476RG Overview and Block Diagram
STM32L476RG Memory Map
STM32 Nucleo64 Board
Bitwise operators in C
Parallel Ports & GPIO
STM32 GPIO Ports
Simple GPIO program without HAL libraries

## Slide 3: STM32L476RG Description (Excerpt)
This text is taken from the STM32L476 DataSheet
See stml476rg.pdf in Resources/Data Sheets
The next few slides are captures from that document

## Slide 4: STM32L476RG Description (Excerpt)

## Slide 5: STM32L476 is a range of devices
Note also that STM32L476xx devices support 7 low power modes

## Slide 6: STM32L476 Block Diagram
This is an important diagram
Especially because of how the Bus Organisation determines what clock to enable to be able to use a given peripheral device
Note also that the I/O from functions like the Timers etc are shared with the GPIO pins
May mean tradeoffs
(See p17 of stm32rg.pdf for better resolution)

## Slide 7: STML476RG Pinout Diagram

## Slide 8: STM32L4xx Naming convention
STM32L476RGT is comes in a 64 pin LQFP package
It has 1 MB of Flash memory

## Slide 9: STM32L4xx Memory Mapping
Not to scale
Note that there are two banks of SRAM
They can be handled differently
Note also that the on-chip peripherals are memory-mapped at addresses 0x4000_0000 and above
This block includes the GPIO block

## Slide 10: STM32L4xx Memory Map of peripherals (Excerpt)
GPIO Block is here
Full table is much longer
Notes: Arm microcontrollers have two types of buses: AHB (Advanced High Performance Bus) and APB (Advanced peripheral Bus).
AHB is a high-performance bus designed to interface to memory and high performance I/O.
APB is designed for lower speed and low power memory and peripherals. APB usually looks like one device on an AHB bus.
So the interface hierarchy is CPU – AHB and CPU – AHB – APB.
Arm microcontrollers need to enable the clock signal for these buses, so this is an extra initialisation task.

## Slide 11: Memory Map boundaries and buses (Excerpt)
GPIO Block is on AHB2 bus
From Reference Manual

## Slide 12: GPIO and Peripheral Memory Map
GPIO, Timers, ADCs etc are memory mapped
They are accessed like addresses in memory but they are located at a fixed range of addresses

## Slide 13: GPIO and Peripheral Memory Map
Each GPIO has a number of registers associated with it
GPIOA_MODER is at 0x4800 0000, GPIOA_ODR is at 0x4800 0014 etc

## Slide 14: Example: GPIO registers and pointers
Notes: The GPIO ports are the most straightforward of the on-chip I/O devices.
At heart it’s just an output port, and input port and a direction register that allows individual bits of a port to be used as an input or as an output.
Using pointers, we can give symbolic names to the ports, even though what is involved is the address of a register.

## Slide 15: Efficient definition of GPIO registers
CMSIS: Cortex Microcontroller Software Interface Standard

## Slide 16: Efficient definition of GPIO registers
This example is not for STML476RG
(Addresses are different)

## Slide 17: Parallel or GPIO Ports
General Purpose Input Output pins are organised as parallel ports with (for STM32) 16 elements
Each one can be an input or output and can also have other advanced options
They are used to drive LEDs, read switches or keypads, etc
Note that microcontroller pins usually have multiple functions because pins are expensive

## Slide 18: Parallel Ports or GPIO Ports
Simplest on-chip I/O devices
You can set an output pin to a logic 1, high voltage level or a logic low, low voltage output under software control
Or read the logic level read in from a pin
Most ports have a similar structure:
A direction register that determines if a pin is to be an output or an input
An output port register
An input pin register

## Slide 19: Simplified structure of a parallel port
One bit of a microcontroller port usually consists of an output port, a direction control register and input register
The STM32 GPIO ports have more features than this port
So more configuration registers are required

## Slide 20: STM32 GPIO Features

## Slide 21: STM32 GPIO Functional Description

## Slide 22: Structure of a GPIO Pin
These options are enabled/disabled using different settings in the GPIO configuration registers.
The output and input registers are also required.
We look at each of the GPIO registers in turn

## Slide 23: Structure of a GPIO 5V tolerant Pin

## Slide 24: GPIO Mode Register
Each GPIO port has 16 bits
Two bits are needed for each pin option
So the mode register needs 32 bits

## Slide 25: GPIO Type Register
Each GPIO port has 16 bits
The default case is the preferred option for most applications
so you may not always need to set up this register

## Slide 26: GPIO Speed Register

## Slide 27: GPIO Pull Up/Down Register
Weak Pull-Up/Pull-Down resistors
Save board real-estate and reduce costs

## Slide 28: GPIO Pull Up/Down Register
Weak Pull-Up/Pull-Down resistors
Save board real-estate and reduce costs

## Slide 29: GPIO Input Data Register
Again, only 16-bits are required

## Slide 30: GPIO Output Data Register
For many MCUs setting individual bits involves a read – mask – rewrite
This involves separate instructions and may not be atomic.
For atomic operations the bit set/reset register may be used (next)

## Slide 31: GPIO Bit Set/Reset Register
Why do you think atomic operations are important?

## Slide 32: GPIO Configuration Lock Register (1)

## Slide 33: GPIO Configuration Lock Register (2)

## Slide 34: GPIO Alternate Function Registers
4 bits per port pin = 64 bits
Two 32-bit registers
The AF patterns allow the pin
To be used for other functions

## Slide 35: GPIO Alternate Function Registers

## Slide 36: GPIO Port Reset Register

## Slide 37: AHB2ENR Register
Other GPIOEN bits are similar
Recall that GPIOs are on the AHB2 Bus

## Slide 38: Nucleo64 STM32L476 Green Led

## Slide 39: Nucleo64 STM32L476 Blue Button

## Slide 40: Example: GPIO registers and pointers

## Slide 41: Example: Using the GPIO registers and pointers
See next slide for how this can be done more efficiently

## Slide 42: Efficient definition of GPIO registers

## Slide 43: Efficient definition of GPIO registers

## Slide 44: Using the technique
Now we can create functions that can be used for each instance of the peripheral
E,g. the code to reset the GPIO port can be written as:

## Slide 45: Using the reset function
Use the function by passing the peripheral base pointer to the function:

## Slide 46: CMSIS
CMSIS: Cortex Microcontroller Software Interface Standard
A consistent software infrastructure for Cortex-M software developers, aims:
Software reuse
Software compatibility
Ease of use
Toolchain independent
Open: CMSIS core files source code can be downloaded from Github
New CMSIS projects have also been released
eg CMSIS-RTOS, CMSIS-DSP, etc

## Slide 47: CMSIS Standardises:
Definitions for the processor’s peripheral registers including:
Nested Vector Interrupt Controller (NVIC)
System tick timer in the processor (SysTick)
Optional Memory Protection Unit (MPU)
Programmable registers in the System Control Block (SCB)
Some software programmable for debugging

## Slide 48: CMSIS Standardises:
Standardized functions to access processor features, including interrupt control functions using NVIC, and functions for accessing special registers in the processors
  You can still access the registers directly, but using the access functions (or Application Programming Interface, API) helps portability
Standardized functions to access special instructions (e.g., Wait- For-Interrupt, WFI)
  Alternatives like intrinsic functions or inline assembly make the software less reusable

## Slide 49: CMSIS Standardises:
Function names for system exception handlers
  Using standardized names makes it easier to develop software solutions across multiple Cortex-M products
  Important for embedded OS developers, as the embedded OS requires the use of several types of system exception.
Functions for system initialization
Modern microcontroller products require some configuration of clock circuitry and power management registers before the application starts
CMSIS-compliant device-driver libraries place these configuration steps in a function called “SystemInit().”
Standardized software variables for clock speed information
This information might be needed for setting up the baud rate divider in a UART, or to initialize the SysTick timer for an embedded
OS
A software variable called “SystemCoreClock” is defined in the CMSIS-Core.

## Slide 50: Summary
Looked at ARM processor and microcontrollers to see where relevant information comes from
Software tools and IDEs
Software Development Flow for some IDEs
Structures of Embedded Software
  Come back to this later
C Data types for embedded development
Microcontroller I/O and software
  Come back to this later too