## Slide 1: ED5502: Digital Systems 4 Embedded Software
Lecture 1:
Introduction
Ciaran MacNamee

## Slide 2: Embedded Systems and Software
Lecturer: Ciaran MacNamee
E-mail: ciaran.macnamee@ul.ie
Room No: ER-2020 (Engineering Research Building)
Tel: 061-213470 (internal: 3470)
Notes: I’ll use the Sulis site for announcements and project submissions, and I’ll announce open office hours this way, when my timetable is stable.

## Slide 3: Embedded Systems and Software: Texts
The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors, by Joseph Yiu
  Newnes, 3rd Edition, ISBN-13: 978-0-12-408082-9
STM32 Arm Programming for Embedded Systems, by Muhammad Ali Mazidi et al
  www.microdigitaled.com
Programming with STM32 Nucleo Boards, by Dogan Ibrahim
  Elektor Publication, ISBN-13: 978-1-907920-68-4
Mastering STM32, by Carmine Noviello (e-book)
  https://leanpub.com/mastering-stm32
There are many other ARM Cortex-M textbooks
Notes: There are many ARM Cortex books around. These are some that I have used in this module. The first is a reference text, and goes into a lot of detail about the Cortex M3 and M4 architecture. The early material is based on this book and I return to it towards the end of the module too.
The other texts are more practical.

## Slide 4: Assessment
Programming is a practical discipline – we learn best by doing
So Module assessment:
Final exam: 30%
Homework assignments: 4 x 5% each (20%)
Labs & Projects: 50%
  Project 1: 20%
  Project 2: 30%

## Slide 5: At the end of this course you should be able to:
Explain how C, assembly, machine code relate to each other
Describe the Cortex M3 and M4 architectures and explain how the elements of the architecture influence how devices are programmed
Program the I/O peripherals in a microcontroller
Program a microcontroller in an embedded system
  In C and possibly in Assembly Language
Build and debug the software for a simple embedded system
Notes: Embedded systems programming takes in a wide variety of programming styles from quite abstract descriptions to low-level operations.
In this module, we are going to look at the detailed organisation of a microcontroller so we will look at the machine code and assembly code running on the device as well as the at the source code that produced it.
The main emphasis will be on programming a microcontroller in a simple embedded system and on debugging our code and getting it working.

## Slide 6: Embedded Microcontrollers
An embedded microcontroller is a microcomputer that contains most of its peripherals and the memory it needs along with a CPU on a single IC
Around for over 35 years: Intel 8051 (8-bit CPU) was one of the earliest MCUs – still widely used
You find it everywhere – window winders in a car, intelligent payment systems – a long list
Other processors include 6801 (sold in billions), PIC, etc
ARM 32-bit MCU has become the dominant 32-bit microcontroller
Notes: A few words on the origins of microcontrollers as opposed to microprocessor devices.
Some of you may be familiar with the 8051 MCU. Today, Arm Cortex devices are dominant 32-bit MCU architecture around – although there are still some other competitors for 32-bit embedded systems design.

## Slide 7: Microcontroller Families
Most microcontrollers come in ranges of families
So you can get many types of 8051 MCU: they differ in the amount of memory, the peripherals (types of I/O) they have, the packages they come in, and so on
Usually you pay for what you get: more memory and I/O costs more
Embedded systems are extremely cost sensitive
You usually try to use the cheapest possible microcontroller that will do the job
Notes: There are many variants of the Arm Cortex M3 and M4, for example. Microcontrollers containing M3 or M4 are also programmed in a similar way but the end use and cost of the devices vary widely.
You pay for higher performance, for more memory and I/O pins. I/O pins are expensive, as are higher clock frequency support and low power modes.
A difference of only a few cents could mean the difference between making and losing money on a given product.
So cost is a big issue.
But time to market is also important – so the good development tools are very important

## Slide 8: ARM Cortex
In this module we use microcontrollers based on the ARM Cortex M3 or M4 core
This microcontroller has an ARM Cortex-M processor core along with on chip program and data memory and I/O peripheral devices that can interface to the real world
You can build an embedded system that is small and low cost with a microcontroller like this
  But ARM is a powerful CPU so it can do very complex operations
  And ARM can be very low power – longer battery life

## Slide 9: ARM Cortex families
ARM processors have many generations
Recent generations are named Cortex
Cortex processors have three profiles
A – High performance (iPads, servers)
R – High performance but deterministic operation for Real-Time (hard drive controllers, automotive drive trains)
M – Deeply Embedded microcontrollers, low power, low cost, high efficiency
Notes: Cortex devices come in different profiles – we use the M profile.

## Slide 10: ARM Families and Architectures
J. Yiu, The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors, 3rd ed, Newnes 2014
Notes: This diagram from Yiu’s book shows the relationships between the Cortex profiles

## Slide 11: ARM Families and Architectures
J. Yiu, The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors, 3rd ed, Newnes 2014
ISA Versions
Notes: The term ISA means Instruction Set Architecture and it determines what the CPU can do.
Arm processors have gone through many generations and unlike x86 generations they are not binary compatible with each other.
Cortex processors may implement v6, v7 or v8 versions of the Arm ISA.
Cortex M3 and M4 (our focus) implement the v7 ISA.
Note that Crtex m0, M0+ and M1 processors implement the earlier (and smaller) v6 ISA

## Slide 12: ARM Cortex M3 and M4
Cortex-M3 (2005) and Cortex-M4 (2010) are 32-bit processors designed by ARM
The Instruction Set Architecture (ISA) used in the Cortex-M processors is the Thumb ISA based on Thumb-2 Technology
  Supports a mixture of 16- and 32-bit instructions
  Earlier ARM processors had separate ARM (32-bit instructions) and Thumb (16-bit instructions) and you had to transition between modes to use each one
Notes: Using a 32-bit instruction word simplifies the CPU design but at the cost of larger code. Using 16-bit instructions reduces code size, at the cost of more decode logic. Some instructions were not available in 16-bit operation, so earlier Arm processors had to switch operating modes from 32-bit Arm instructions to 16-bit Thumb instructions.
Arm ISA v7 contains 16-bit and 32-bit instructions so you don’t need to transition between modes – this is a better option for programmers.

## Slide 13: ARM Cortex M3 and M4 features (1)
Three-stage pipeline
Harvard bus architecture with unified memory space: same address space for instructions and data
  (von Neumann at ISA level, Harvard at implementation level)
On-chip bus interfaces based on AMBA
NVIC interrupt controller: up to 240 interrupt requests and 8 to 256 interrupt priority levels
Support for implementing OS: system tick timer, shadowed stack pointer
Notes: Some architecture details.
Note:
von Neumann architecture: single memory space for code and data
Harvard architecture: separate code and data memory spaces
Many modern CPUs are von Neumann at the ISA level, but Harvard atht eth implementation level.
What are the advantages of doing this?
Also note that Arm has a very powerful interrupt mechanism and has built-in support for operating system design.

## Slide 14: ARM Cortex M3 and M4 features (2)
Sleep mode and other low power features
Support for optional Memory Management Unit (MMU)
Bit Band: support for bit-data accesses in two specific memory areas
Can be used in single-processor or multiple processor designs
Notes: These are desirable embedded system features.

## Slide 15: ARM Cortex M3 and M4 ISA
General data processing, including hardware multiplication and division
Memory access instructions support 8-, 16-, 32- and 64-bit data and multiple 32-bit data transfers
Bit-field processing instructions
Multiply Accumulate (MAC) and saturate instructions
Unconditional and conditional Branches and function calls
Instructions for system control, OS support etc
ISA: Instruction Set Architecture
Notes: A summary of aspects of the ISA

## Slide 16: ARM Cortex M4 ISA
Single instruction multiple data (SIMD) operations
Additional fast MAC and multiply instructions
Saturating arithmetic instructions
Optional floating point instructions (M4F option)
These instructions are available in the M4 variant only
(Not in M3)

## Slide 17: ARM Cortex M family
Cortex-M3 and –M4 are based on the ARMv7-M architecture
Cortex-M0+, -M0 and –M1 (for FPGAs) processors are based on the ARMv6-M architecture (smaller ISA)
Choice of processor depends on the end application
Older ARM7, ARM9 processors are not Cortex processors
Notes: Arm Cortex M0 designs are very low cost, hence the emphasis is on a smaller CPU core – lower area so lower cost.

## Slide 18: Cortex-M processor family
Notes: This illustrates the end use and performances to be expected form different Cortex processor or processor cores.

## Slide 19: Cortex-M processor family
Relationships between Instruction Set Architecture Versions
Notes: This slide illustrates the relationships between Instruction Set Architecture Versions for M profile Cortex devices.
Cortex M3 and M4 are quite similar. M4 is s superset of M3.

## Slide 20: ARM Processors and Microcontrollers
ARM does not make microcontrollers: it designs Processors
  ARM processors are licensed to manufacturers who design microcontrollers using ARM cores
A microcontroller contains a processor and also on-chip memory and hardware I/O modules like ADCs, Ports, Timers etc
Semiconductor companies license ARM processors and surround the processor with I/O modules and varying amounts of memory
  This differentiates products from each other
Notes: One of the key points about Arm is that Arm processors are designed by Arm, but sold as IP to semiconductor manufacturers.
Analog Devices, NXP, ST microelectronics, Texas Instruments and many others licence Arm core designs and build a microcntroller around the Arm Core – we’ll see an example next slide.

## Slide 21: ARM Cortex-M4 based microcontroller
CPU is just one part of the microcontroller
Notes: This is a typical Cortex M4 microcontroller. (This one is a Kinetis microcontroller, now supplied by NXP).
You can see that the Arm processor is just one component of the microcontroller. The semiconductor manufacturer has designed and implemented (or re-used) the other blocks that define the microcontroller’s overall functionality. Other devices would have a different mix of on-chip functional modules or might have more or less memory, or might run at different clock frequencies.

## Slide 22: Features of ARM Cortex M Processors
Low Power, High Performance, Energy Efficient
Code Density
Interrupts: Configurable interrupt controller
Ease of use, C friendly, Scalable
Debug support
OS support
Software portability
Wide range of support tools from multiple vendors
Notes: Advantages of ARM Cortex M Processors
Low Power: ARM cores are small and designed for low power consumption
High Performance: Cortex M3/M4 score highly using established perfomance benchmarks
Energy Efficiency
Code Density: Thumb-2 ISA can encode many instructions in 16-bits, meaning the amount of memory to realise a given program or task can be minimised
If you can fit your program in a smaller memory you can reduce costs
Interrupts: The Cortex M3/M4 interrupt controller is configurable, supporting up to 240 vectored interrupts and multiple levels of interrupt priorities
Ease of use, C friendly: Simple Cortex memory map supports efficient C compilers
Scalability
Debug features: very important for time-to-market reasons
OS support
Software portability
Widely range of support tools from multiple vendors

## Slide 23: C and C++ Programming Languages
All processors execute binary or machine code
  But you can generate machine code in many ways
The closest thing to machine code is to program in assembly language
  Gives great insight into the details of the microcontroller
  But assembly programming is processor dependent – not portable – and often is more detailed than you want
C is a high level programming language that allows access to the low level resources of a microcontroller but is easier to use
We use C and possibly a small amount of assembly
Notes: As you know, a processor executes binary machine code. This slide illustrates how the machine code is produced from the source files that you write.
C and C++ are commonly used embedded software programming languages, though scripting languages like Python are starting to become popular too. For this module we use C, and possibly some assembly code.

## Slide 24: Computer instructions are in bits
Computer instructions are formed from binary bits
The instructions are simple operations such as arithmetic and logical operations like Add, Subtract, Move data, Test a condition and so on
These instructions are what the computer can do
The CPU fetches the binary patterns, decodes them and completes executing the specified operation
Notes: A graphic showing program fetch from memory to the processor.
Note that I tend to use the terms CPU (Central Processing Unit), MPU (Micro Processing Unit), processor and microprocessor interchangeably.

## Slide 25: Higher level computer languages
This is how High Level Computer Languages, Assembly Language and Machine code are related
For programming, we use tools to generate lower level code from higher level code
Notes: A graphic showing the relationships between C source, assembly code and machine code. This is shown for ARM v8, but it’s the same for ARM v7.

## Slide 26: Support tools
ARM provides many tools to support chip design based on ARM processors as well as tools to support ARM software development
Many third-party vendors also provide ARM software development tools and IDEs
  IDE: Integrated Development Environment - typically includes a compiler, linker, program loader or flash programming tool as well as debugging tools all within the same Environment
  Keil-MDK for Arm microcontrollers
  Atollic IDE for STM32 Cortex-M microcontrollers
Notes: Development support tools are essential for programming embedded systems. We are using the STM32L476RG microcontroller in an ST Nucleo-64 development board. It is supported by a number of powerful development environments, including Keil, mbed and Atollic. The Atollic IDE is based on the Eclipse and uses the open source GNU compiler collection (gcc) C compiler, linker and also includes a debugging interface.

## Slide 27: STM32 and ARM
ST Microelectronics is an ARM Cortex-M licensee: produces Cortex-M microcontrollers under the generic name STM32
The STM32 portfolio includes Arm®Cortex®-M cores (M0, M0+, M3, M4 and M7)
STM32 feature: it’s easy to port applications from one device to another
Devices have similar pinouts and are supported by good tools
STM32 & the Atollic TrueStudio IDE, or Keil
Notes: ST Microcontroller produces a wide range of microcontrollers based on the various Cortex cores.

## Slide 28: Summary
Overview of ARM Cortex-M microcontrollers and place of M3 and M4 in the family
Overview of Cortex M3 and M4 features